ToE Address Map (Dunc's Machine).

E7	TOE_MemptrLo

E8	TOE_MemptrHi

Together, zero page variables form a 16 bit address used by assorted functions in the ToE firmware.

5E0	MON_sysvars system variable. This is the Output options bit-field. Bits are set according to which service is enabled.

Bit 0 controls ACIA output
Bit 1 controls the ANSI output
Bit 2 controls the TPB Centronics output.

5E1	os_infilt system variable. This controls whether or not to filter out line feed characters or not ($A).

C000-C00F	ANSI Video card's 6522 VIA (agreed standard location)

C010-C013	65C51 Serial Port (as coded in ROM for keyboard currently)

C014-C017	65c51 Serial Port 2 (general purpose serial port)

C020-C02F	TPB IO Bus Card VIA (with currently committed ROM firmware)

C030-C038	SCC2691 UART Serial Card (not currently fitted)

C040-C04F	6522 VIA card (when fitted)

C0E0-C0EF	6522 VIA for V3 Sound Card. (agreed standard location at present)

C0FC-C0FD	AY-3-8912A Sound Card (agreed standard location. Not fitted)

C0FF	Bank Register (Fixed Location, write only)

Page selection bits by bank:

xxxx1234

NOTE:- Don't page the ROM from EhBASIC whilst interrupts are being run as the system will crash!
FF90	ANSI_init_vec	Initialises the ANSI card.

FF93	ANSI_write_vec	Writes the contents of the A register to the ANSI card.

FF96	TPB_init_vec	Initialises the Tower Peripheral Bus card.

FF99	TPB_LPT_write_vec	Writes the contents of the A register to the LPT port.

FF9C	TPB_tx_byte_vec	Transmits the contents of the A register to the TPB bus.

FF9F	TPB_tx_block_vec	Transmits the contents of TPB_BUS_blk_st for	TPB_BUS_blk_len bytes.

FFA2	TPB_ATN_handler_vec

FFA5	TPB_rx_byte_vec

FFA8	TPB_rx_block_vec

FFAB	TPB_Dev_Presence_vec

FFAE	TPB_Req_Dev_Type_vec

FFB1	TPB_dev_select_vec

FFB4	TPB_Ctrl_Blk_Wr_vec

FFB7	TPB_Ctrl_Blk_Rd_vec

FFBA	TAPE_Leader_vec

FFBD	TAPE_BlockOut_vec

FFC0	TAPE_ByteOut_vec

FFC3	TAPE_BlockIn_vec

FFC6	TAPE_ByteIn

FFC9	TAPE_init_vec

FFCC	TAPE_SAVE_BASIC_vec

FFCF	TAPE_LOAD_BASIC_vec

FFD1	TOE_PrintStr_vec